I2S – Inter-IC Sound
Akshata Mukund Shetty

---
Contents
- Introduction
- Modes of I2S module
- Features
- Example
- I2S configuration API's

---
Introduction
- I²S (Inter-IC Sound) is an electrical serial bus interface standard used for connecting digital audio devices together.
- The bus can handle audio data.
- A 3-line serial bus is used consisting of a line for two time-multiplexed data channels, a word select line and a clock line.

---
Introduction
The bus has three lines:
   • continuous serial clock (SCK);
   • word select (WS);
       WS = 0; channel 1 (left);
       WS = 1; channel 2 (right).
  • serial data (SD);
      serial data (SD) can be called SDATA, SDIN, SDOUT, DACDAT,
      ADCDAT, etc
 The device generating SCK and WS is the master.

---
Introduction

---
Different modes of I2S module
The I2S module has three modes:
- Master
- Controller
- Slave

---
Features
- 8 - 32 data bits per sample
- 16, 32, 48, or 64 bit word select period
- Data rate up to 192 kHz with 64 bit word select period: 12.288 MHz.
- Tx and Rx FIFO interrupts
- DMA support
- Independent left and right channel FIFOs
- Independent enable of Rx and Tx

---
Example of I2S configuration
#include "driver/i2s.h"
#include "freertos/queue.h"
static const int i2s_num = 0; // i2s port number
static const i2s_config_t i2s_config = {
   .mode = I2S_MODE_MASTER | I2S_MODE_TX,
   .sample_rate = 44100,
   .bits_per_sample = 16,
   .channel_format = I2S_CHANNEL_FMT_RIGHT_LEFT,
   .communication_format = I2S_COMM_FORMAT_I2S|I2S_COMM_FORMAT_I2S_MSB,
   .intr_alloc_flags = 0, // default interrupt priority
   .dma_buf_count = 8,
   .dma_buf_len = 64,
   .use_apll = 0
};

---
Example of I2S configuration
static const i2s_pin_config_t pin_config = {
    .bck_io_num = 26,
    .ws_io_num = 25,
    .data_out_num = 22,
    .data_in_num = I2S_PIN_NO_CHANGE
};
…
i2s_driver_install(i2s_num, &i2s_config, 0, NULL); //install and start i2s driver
i2s_set_pin(i2s_num, &pin_config);
i2s_set_sample_rates(i2s_num, 22050); //set sample rates
i2s_driver_uninstall(i2s_num); //stop & destroy i2s driver

---
I2S configuration API's
- void I2S_init(void) : Enables the I2S interface
- void I2S_start(void) : Starts the I2S interface.
- void I2S_stop(void) : Disables the I2S interface.
- void I2S_enableTx(void) : Enables the Tx direction of the I2S interface.
- void I2S_disableTx(void) : Disables the Tx direction of the I2S interface.
- void I2S_enableRx(void) : Enables the Rx direction of the I2S interface.
- void I2S_disableRx(void) : Disables the Rx direction of the I2S interface.

---
I2S configuration API's
uint8 I2S_readRxStatus(void) : Returns state in the I2S Rx status register
- uint8 I2S_readTxStatus(void) : Returns state in the I2S Tx status register
- uint8 I2S_readByte(uint8 word_Select) : Returns a single byte from the Rx FIFO.
- void I2S_writeByte(uint8 wrData, uint8 word_Select) : Writes a single byte into the Tx FIFO.
- void I2S_clearRxFIFO(void) : Clears out the Rx FIFO.
- void I2S_clearTxFIFO(void) : Clears out the Tx FIFO.
- void I2S_sleep(void) : Saves configuration and disables the I2S interface
- void I2S_wakeUp(void) : Restores configuration and enables the I2S interface